## Slide 1
UNIT – IV
Programmable Logic devices, Memory and Logic Families

## Slide 2: Programmable Logic Devices (PLD)
Programmable Logic Devices (PLDs) are IC chips with internal logic gates connected by electronic fuses.
These fuses can be ‘blown’ (by programming) to obtain different circuit configurations.
Semi-customized chips that give high packing density at reasonable cost.
Three classes of PLDs are :
  Programmable Logic Array (PLA)
  Programmable Read Only Memory (PROM)
  Programmable Array Logic (PAL)

## Slide 3: Programmable Logic Devices
Fixed
AND array
Fused
programmable
OR array
Fuses
Inputs
Outputs
Fixed
OR array
Fused
programmable
AND array
Fuses
Inputs
Outputs
Inputs
Fused
programmable
OR array
Fuses
Outputs
Fuses
Fused
programmable
AND array
Programmable Read Only Memory (PROM)
Programmable Array Logic (PAL)
Programmable Logic Array (PLA)

## Slide 4: Programmable Logic Array (PLA)
Combination of a programmable AND array followed by a programmable OR array.
Example: Design a PLA to realise the following three logic functions and show the internal connections.
f1(A,B,C,D,E) = A'.B'.D' + B'.C.D' + A'.B.C.D.E'
f2(A,B,C,D,E) = A'.B.E + B'.C.D'.E
f3(A,B,C,D,E) = A'.B'.D' + B'.C'.D'.E + A'.B.C.D

## Slide 5: Realising Logic Functions with PLAs
f1(A,B,C,D,E) = A'.B'.D' + B'.C.D' + A'.B.C.D.E'
f2(A,B,C,D,E) = A'.B.E + B'.C.D'.E
f3(A,B,C,D,E) = A'.B'.D' + B'.C'.D'.E + A'.B.C.D
A
B
C
D
E
P1
P3
P4
P6
P5
P2
P7
Programmable OR array
Programmable AND array
A'B'D'
X
X
X
B'CD'
X
X
X
X
X
X
X
X
A'BCDE'
A'BE
X
X
X
X
X
X
X
B'CD'E
B'C'D'E
X
X
X
X
A'BCD
X
X
X
X
f1
f2
f3
X
X
X
X
X
X
X
X
A'.B'.D'
B'.C.D'
A'.B.C.D.E'