## Slide 1: Unit - 3
Combinational Logic Circuits

## Slide 2: Contents
Binary adder
Binary adder as subtractor
Carry look ahead adder
Decimal adder
Magnitude Comparator

## Slide 3: Binary adder
HA
x
y
S
C
Binary Adder

## Slide 4: Half adder
Binary Adder
X
Y
X
Y

## Slide 5: Binary Adder
Full Adder
  Adds 1-bit plus 1-bit plus 1-bit
  Produces Sum and Carry
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
x
+ y
+ z
───
C S
FA
x
y
z
S
C
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 0 | 1 | 0
x |  | 0 | 1 | 1 | 1
 |  |  | z |  | 
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz

## Slide 6: Binary Adder
Full Adder
x
y
z
S
C
x
y
z
S
C
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz

## Slide 7: Binary Adder
Full adder design from two half adder

## Slide 8: Binary Adder
Full Adder
HA
x
y
z
HA
S
C

## Slide 9: Binary Adder
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0

## Slide 10
Binary Adder
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy

## Slide 11
Input |  | Output | 
A | B | Difference (D) | Borrow (Bout)
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Block schematic of half-subtractor
Binary Subtractor
Truth table
Logical expression
Logical design

## Slide 12
Inputs |  |  | Outputs | 
A | B | Bin | Difference(D) | Borrow(Bout)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
Binary Subtractor
Block schematic of full-subtractor
Truth table
Logical expression

## Slide 13
Binary Subtractor
Logical design

## Slide 14
1’s Complement of a Binary Number
There is a simple algorithm to convert a binary number into 1’s complement. To get 1’s complement of a binary number, simply invert the given number.
2’s Complement of a Binary Number
There is a simple algorithm to convert a binary number into 2’s complement. To get 2’s complement of a binary number, simply invert the given number and add 1 to the least significant bit (LSB) of given result.
Binary Subtractor
Example

## Slide 15: Binary Subtractor
Use 2’s complement with binary adder
  x – y = x + (-y) = x + y’ + 1

## Slide 16
Binary Subtractor

## Slide 17: Binary Adder/Subtractor
M: Control Signal (Mode)
  M=0  F = x + y
  M=1  F = x – y

## Slide 18
Binary Subtractor

## Slide 19
Carry look ahead Adder
Full adder equation
AB+ (A XOR B)C

## Slide 20
Carry look ahead Adder

## Slide 21
Carry look ahead Adder

## Slide 22: Decimal Adder
A decimal adder requires a minimum of 9 inputs and 5 outputs
1 digit requires 4-bit
Input: 2 digits + 1-bit carry
Output: 1 digit + 1-bit carry
BCD adder
Perform the addition of two decimal digits in BCD, together with an input
carry from a previous stage.
The output sum cannot be greater than 19 (9+9+1)

## Slide 23: BCD Adder
4-bits plus 4-bits
Operands and Result: 0 to 9
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0
0 + 0 | 0 0 0 0 | 0 0 0 0 | = 0 | 0 | 0 0 0 0
0 + 1 | 0 0 0 0 | 0 0 0 1 | = 1 | 0 | 0 0 0 1
0 + 2 | 0 0 0 0 | 0 0 1 0 | = 2 | 0 | 0 0 1 0
0 + 9 | 0 0 0 0 | 1 0 0 1 | = 9 | 0 | 1 0 0 1
1 + 0 | 0 0 0 1 | 0 0 0 0 | = 1 | 0 | 0 0 0 1
1 + 1 | 0 0 0 1 | 0 0 0 1 | = 2 | 0 | 0 0 1 0
1 + 8 | 0 0 0 1 | 1 0 0 0 | = 9 | 0 | 1 0 0 1
1 + 9 | 0 0 0 1 | 1 0 0 1 | = A | 0 | 1 0 1 0
2 + 0 | 0 0 1 0 | 0 0 0 0 | = 2 | 0 | 0 0 1 0
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 12 | 1 | 0 0 1 0
Invalid Code
Wrong BCD Value
0001 1000

## Slide 24: BCD Adder
X +Y | x3 x2 x1 x0 | y3 y2 y1 y0 | Sum | Cy | S3 S2 S1 S0 | Required BCD Output | Value
9 + 0 | 1 0 0 1 | 0 0 0 0 | = 9 | 0 | 1 0 0 1 | 0 0 0 0 1 0 0 1 | = 9
9 + 1 | 1 0 0 1 | 0 0 0 1 | = 10 | 0 | 1 0 1 0 | 0 0 0 1 0 0 0 0 | = 16
9 + 2 | 1 0 0 1 | 0 0 1 0 | = 11 | 0 | 1 0 1 1 | 0 0 0 1 0 0 0 1 | = 17
9 + 3 | 1 0 0 1 | 0 0 1 1 | = 12 | 0 | 1 1 0 0 | 0 0 0 1 0 0 1 0 | = 18
9 + 4 | 1 0 0 1 | 0 1 0 0 | = 13 | 0 | 1 1 0 1 | 0 0 0 1 0 0 1 1 | = 19
9 + 5 | 1 0 0 1 | 0 1 0 1 | = 14 | 0 | 1 1 1 0 | 0 0 0 1 0 1 0 0 | = 20
9 + 6 | 1 0 0 1 | 0 1 1 0 | = 15 | 0 | 1 1 1 1 | 0 0 0 1 0 1 0 1 | = 21
9 + 7 | 1 0 0 1 | 0 1 1 1 | = 16 | 1 | 0 0 0 0 | 0 0 0 1 0 1 1 0 | = 22
9 + 8 | 1 0 0 1 | 1 0 0 0 | = 17 | 1 | 0 0 0 1 | 0 0 0 1 0 1 1 1 | = 23
9 + 9 | 1 0 0 1 | 1 0 0 1 | = 18 | 1 | 0 0 1 0 | 0 0 0 1 1 0 0 0 | = 24
+ 6










## Slide 25: BCD Adder
Correct Binary Adder’s Output (+6)
  If the result is between ‘A’ and ‘F’
  If Cy = 1
S3 S2 S1 S0 | y1
0 0 0 0 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 1
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
 |  |  |  | S1 |  |  | 
 |  |  |  |  |  | S2 | 
S3 |  | 1 | 1 | 1 | 1 |  | 
 |  |  |  | 1 | 1 |  | 
 |  |  | S0 |  |  |  | 
Err = S3 S2 + S3 S1

## Slide 26: BCD Adder
Err

## Slide 27
BCD Adder

## Slide 28: Overflow
Unsigned Binary Numbers
2’s Complement Numbers
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Carry
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Overflow

## Slide 29
A comparator used to compare two bits is called a single bit comparator.
It consists of two inputs each for two single bit numbers and three outputs to generate less than, equal to and greater than between two binary numbers.
Truth table
Magnitude Comparator
Equation from truth table
Logic design
1- Bit magnitude comparator

## Slide 30
A comparator used to compare two binary numbers each of two bits is called a 2-bit Magnitude comparator. It consists of four inputs and three outputs to generate less than, equal to and greater than between two binary numbers.
2- Bit magnitude comparator
Truth table
Magnitude Comparator

## Slide 31
K map for 2- Bit magnitude comparator
Design equations

## Slide 32
Logic design of 2 –bit magnitude comparator