## Slide 1: Unit - 4
Flip Flops

## Slide 2: Combinational Logic
The outputs depend only on the state of the inputs all of the time. Any change in the state of one of the inputs will ripple through the circuit immediately.
  Examples of combinational logic are NAND and NOR gates, Inverters, and Buffers. These four logic gates form the basis of almost all combinational logic circuits as well as flip flops.

## Slide 3: Sequential Logic
Has memory; the circuit stores the result of the previous set of inputs. The current output depends on inputs in the past as well as present inputs.
  The basic element in sequential logic is the bistable latch or flip-flop, which acts as a memory element for one bit of data.
Combinational logic
Memory elements
Combinational outputs
Memory outputs
External inputs
Sequential circuit = Combinational logic + Memory Elements

## Slide 4: Digital Circuits
Combinational Logic Circuit
Sequential Logic Circuit
0
1
0
1
0
1
1
1
0
1
1
0
A
B
C
D
Y
- output depends on present inputs
- consisted of logic gates and combinational logic subsystems (multiplexer, etc)
outputs
Sequential Logic Circuit
present inputs
previous outputs
- output depends on present inputs and previous outputs
- enable or clock signal is used to synchronize the output change with time
Enable
or Clock

## Slide 5
Enable
or Clock
LATCHES and FLIP-FLOPS
Temporary Storage
Bistable Device
2 outputs
0
1
Q
Q
0
1
1
0
0
1
Q
Q
0
1
1
0
0
1
RESET
SET
(Q=0)
(Q=1)
Some Applications:
Memory
Counters
Shift Register
-cover in DF2
1
1
0
1
0
0
0
0
0
0
0
1
0
0
1
0
0
0
1
1
0
1
0
0
0
1
0
1
1
0
0
1
0
1
1
1

## Slide 6
Latches
Gated Latches
Flipflops (FF)
SR Latch
Gated SR Latch
SR FF
Gated D Latch
D FF
JK FF
Active HIGH inputs
S
R
Q
Q
S
R
Q
Q
EN
D
Q
Q
EN
S
R
Q
Q
CLK
D
Q
Q
CLK
J
K
Q
Q
CLK
Active LOW inputs

## Slide 7: Latches --SR Latch
The SR latch is a circuit with two cross-coupled NOR gates or two cross-coupled NAND gates. It has two inputs labeled S for set and R for reset.

## Slide 8: SR Latch with Control Input
The operation of the basic SR latch can be modified by providing an additional control input that determines when the state of the latch can be changed. In Fig. 5-5, it consists of the basic SR latch and two additional NAND gates.

## Slide 9: Flip Flops Vs Latches
A flip flop is an electronic circuit with two stable states that can be used to store binary data.
The stored data can be changed by applying varying inputs.
Latches and flip-flops are circuit elements whose output depends not only on the current inputs, but also on previous inputs and outputs.
The difference between a latch and a flip-flop is that a latch does not have a clock signal, whereas a flip-flop always does.

## Slide 10: Latch VS Flipflop

## Slide 11: Exercise 1
Draw the output waveform for the S, R inputs shown below for an active high input SR latch
Assume Q=0 initially
S
R
Q
set
No change
reset
No change
reset
No change
set
No change
S
R
Q
Q
1
0
0
0
0
1
0
0
0
1
0
0
1
0
0
0

## Slide 12: Gated Latches
S
R
Q
Q
EN
S
R
EN
Q
0
1
0
1
0
1
0
0
1
0
Set
Assume Q=0 initially
Reset
Set
No change
Reset
1. Gated SR Latch
1
1
1
1
1
EN = 0 No change
EN = 0 No change
 | S | R | Q
 | 0 | 0 | No change
 | 0 | 1 | 0 (Reset)
 | 1 | 0 | 1 (Set)
 | 1 | 1 | Invalid
EN
1
1
1
1
0
x
x
No change

## Slide 13
SR Flip Flop
JK Flip Flop
D Flip Flop
T Flip Flop
A Flip Flop is a memory element that is capable of storing one bit of information.
Flipflops
A flip flop can maintain a binary state for an unlimited period of time as long as-
(i) Power is supplied to the circuit.
(ii) or until it is directed by an input signal to switch states
Types of Flipflops

## Slide 14: Steps to design of Flipflops
Circuit diagram using universal gates
Truth Table
Characteristics Equation
Excitation Table
State Diagram
Timing (or) Switching (or) Waveform Diagram

## Slide 15: S-R Flip flop
C | S | R | Qn | Qn+1 | State of Operation
1 | 0 | 0 | 0 | 0 | hold
1 | 0 | 0 | 1 | 1 | 
1 | 0 | 1 | 0 | 0 | clear (reset)
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 0 | 1 | set
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 0 | ? | indeterminate
1 | 1 | 1 | 1 | ? | — avoid
(i) Circuit diagram
(ii) Truth Table

## Slide 16
(iii) Characteristic Equation
(iv) Excitation Table
(v) State Diagram

## Slide 17: Gated Latch
Q
Q
EN
EN = 1, normal latch operation
EN = 0, no change in output even when inputs change
Flip-flop
Q
Q
CLK
Level enabled
S
R
0
1
1
0
1
1
0
1
0
0
0
1
1
0
Edge-triggered
Q
Q
CLK
CLOCK (CLK) signal
0
0
0
0
1
1
1
1
Positive-going edge
1
1
1
1
0
0
0
0
Negative-going edge
PGT FF
NGT FF
1
0
1
0
0
1
1
0
1
0
0
1
S
R
S
R

## Slide 18
(V) Timing (or) Switching (or) Waveform Diagram
When Qn=1
C | S | R | Qn | Qn+1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | ?
1 | 1 | 1 | 1 | ?

## Slide 19
S
R
S
R
Q
Q
CLK
Assume Q=0 initially
CLKA
0
1
0
1
0
1
Set
Reset
Set
Complete the timing diagrams shown below
CLK
Q
S
R
CLKA
Q
S
R
Q
Q
CLK
Assume Q=1 initially
Set
Reset
No change
CLKA
0
0
0
1
0
1

## Slide 20: D - Flip flop
(i) Circuit diagram
(ii) Truth Table
C | D | Qn | Qn+1 | State of Operation
1 | 0 | 0 | 0 | Clear (reset)
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | Set
1 | 1 | 1 | 1 | 

## Slide 21
(iii) Characteristic Equation
(iv) Excitation Table
(v) State Diagram
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 22
(V) Timing (or) Switching (or) Waveform Diagram
When Qn=1
C | D | Qn | Qn+1 | State of Operation
1 | 0 | 0 | 0 | Clear (reset)
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | Set
1 | 1 | 1 | 1 | 

## Slide 23
D
Q
0
0
1
D
Q1
Complete the timing diagrams shown below
Assume Q1=0 initially
D
Q
Q
CLK
CLKA
CLKA
D
Q1
Q1
CLK
CLKA
Assume Q=0 initially
CLKA
1
0
0

## Slide 24: J-K Flip flop
C | J | K | Qn | Qn+1 | State of Operation
1 | 0 | 0 | 0 | 0 | hold
1 | 0 | 0 | 1 | 1 | 
1 | 0 | 1 | 0 | 0 | clear (reset)
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 0 | 1 | set
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 0 | 1 | 
1 | 1 | 1 | 1 | 0 | Toggle
(i) Circuit diagram
(ii) Truth Table

## Slide 25
(iii) Characteristic Equation
(iv) Excitation Table
(v) State Diagram

## Slide 26
(V) Timing (or) Switching (or) Waveform Diagram
When Qn=1

## Slide 27
J
K
Q
Q
CLK
J
K
CLKA
Q
No change
Toggle
Toggle
Set
Reset
J
K
Q
No change
Toggle
Set
No change
J
K
Q
Q
CLK
Assume Q=0 initially
Assume Q=0 initially
CLKA
CLKA
CLKA
0
0
1
1
1
1
0
1
1
0
0
0
1
1
0
1
0
0

## Slide 28: T Flipflop
(i) Circuit Diagram (ii) Truth Table

## Slide 29
(iii) Characteristic Equation
(iv) Excitation Table

## Slide 30
(v) State Diagram
(vi) Timing Diagram

## Slide 31: Race around condition in JK FF

## Slide 32: Master slave JK flipflop

## Slide 33: Master slave JK flipflop

## Slide 34: Master slave JK flipflop

## Slide 35: Excitation Tables
RS FLIP FLOP |  |  |  |  |  |  | 
Truth Table |  |  |  | Excitation Table |  |  | 
S | R | Qn+1 |  | Qn | Qn+1 | S | R
0 | 0 | Qn |  | 0 | 0 | 0 | X
0 | 1 | 0 |  | 0 | 1 | 1 | 0
1 | 0 | 1 |  | 1 | 0 | 0 | 1
1 | 1 | X |  | 1 | 1 | X | 0
JK FLIP FLOP |  |  |  |  |  |  | 
Truth Table |  |  |  | Excitation Table |  |  | 
J | K | Qn+1 |  | Qn | Qn+1 | J | K
0 | 0 | Qn |  | 0 | 0 | 0 | X
0 | 1 | 0 |  | 0 | 1 | 1 | X
1 | 0 | 1 |  | 1 | 0 | X | 1
1 | 1 | Qn’ |  | 1 | 1 | X | 0
T FLIP FLOP |  |  |  |  |  | 
Truth Table |  |  |  | Excitation Table |  | 
T | Qn | Qn+1 |  | Qn | Qn+1 | T
0 | 0 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 1 | 0 |  | 1 | 1 | 0
D FLIP FLOP |  |  |  |  |  | 
Truth Table |  |  |  | Excitation Table |  | 
D | Qn | Qn+1 |  | Qn | Qn+1 | D
0 | 0 | 0 |  | 0 | 0 | 0
0 | 1 | 0 |  | 0 | 1 | 1
1 | 0 | 1 |  | 1 | 0 | 0
1 | 1 | 1 |  | 1 | 1 | 1