## Slide 1: SHIFT REGISTERS

## Slide 2
S-1 | SLO-1 | Registers and Types of Registers- Serial In - Serial Out, Serial In - Parallel out
 | SLO-2 | Parallel In - Serial Out, Parallel In - Parallel Out

## Slide 3
Slides 3
REGISTERS
Shift registers are types of sequential logic circuits closely related to digital counters used primarily for the storage of data

## Slide 4
Q → 1 at the clock NGT
1
transfer 1 from input to output
CLK
D
CLK
Q
Q → 0 at the clock NGT
transfer 0 from input to output
Q
0
D
CLK
0
CLK
1
Q
Q
Slides 4
DATA STORAGE
Notes: 4

## Slide 5
Storage capacity (number of bits) of a register is determined by the number of flip-flops
  - One flip flop represents one bit of data storage
  - “n” number of flip-flops can store an n-bit data
The FFs interconnection should facilitate
  - transfer of binary data into and out of the register, and
  shifting data within the register one or more bit positions left or right, effected upon the application of clock pulses
If no clock pulses are applied, there will be no data shift in the register
DATA STORAGE AND SHIFT
Slides 5
Notes: 5

## Slide 6
Data can written in and read out from a register either serially (one bit at a time) or in parallel (all bits simultaneously)
Din
Data In
Data Out
Serial In Parallel Out (SIPO)
Q
Q
Q
Q
Din
Data In
Data Out
Serial In Serial Out (SISO)
Din
Parallel In Parallel Out (PIPO)
Din
Din
Din
Q
Q
Q
Q
Q
Din
Data In
Parallel In Serial Out (PISO)
Din
Din
Din
Q
Data Out
Data In
Data Out
DATA MANIPULATION
Slides 6
Notes: 6

## Slide 7
Type 1 - Serial In Parallel Out (SIPO)
  Data bits are entered serially into the shift register.
  Each bit appears on its respective output line, and all bits are available simultaneously.
Type 2 - Serial In Serial Out (SISO)
  The serial in serial out shift register accepts data serially, i.e. one bit at a time on a single line.
  It produces stored information on its output also in serial form.
4 TYPES OF DATA MOVEMENT
Slides 7
Notes: 7

## Slide 8
Type 3 - Parallel In Serial Out (PISO)
  Data bits are entered simultaneously into their respective stages in parallel fashion.
  The output is serial i.e. shifting one bit at a time on a single line.
Type 4 - Parallel In Parallel Out (PIPO)
  Data bits are entered simultaneously into their respective stages in parallel. All bits are also available at the respective output stage in parallel.
4 TYPES OF DATA MOVEMENT
Slides 8
Notes: 8

## Slide 9: SIPO Register Basic Operation
Accepts data serially on bit by bit basis
Once data is stored, each data bit appears simultaneously on its respective output line
Application of SIPO:
  - A computer or microprocessor based system commonly processes data in parallel format.
  - Hence, serial incoming data is converted into parallel format through a SIPO register
Slides 9
Notes: 9

## Slide 10: Example 1: 4-bit Shift SIPO Register
CLK | Din | Q0 | Q1 | Q2 | Q3
Initial |  |  |  |  | 
T1 |  |  |  |  | 
T2 |  |  |  |  | 
T3 |  |  |  |  | 
T4 |  |  |  |  | 
Show the contents of the register for the data input and clock given. Initial register value is 0.
FF0
FF1
Q0
Q1
D0
D1
FF2
FF3
Q2
Q3
D2
D3
Q0
Q1
Q2
Q3
CLK
Din
Data Input (Din)
CLK
Q0
Q1
Q2
Q3
T1
T2
T3
T4
0
0
0
0
1
0
1
0
1
0
0
0
0
1
0
0
1
0
1
0
0
1
0
1
x
Slides 10
SERIAL
PARALLEL OUTPUTS
Notes: 10

## Slide 11: SISO Register Basic Operation
Data is shifted into the register on bit by bit basis.
After the data is stored completely, it can be shifted out serially upon further application of the clock pulses
Application of the SISO Register
  - The SISO shift register can be used to provide a time delay from input to output.
  - This delay is a function of the number of FFs in the register and clock period.
Slides 11
Notes: 11

## Slide 12: 4-bit SISO shift register using D-FFs
Data Advance (clock) connected to PGT → Data is shifted when clock signal changes from 0 to 1
FF0
FF1
Q0
Q1
D0
D1
FF2
FF3
Q2
Q3
D2
D3
Data Output
CLK
Data Input
Slides 12
SERIAL
SERIAL
Notes: 12

## Slide 13: Example 2: 3-bit shift SISO register
Show the state of the output Q of the 3-bit SISO register for the data input and clock given. Initial register value is 0.
CLK | Din | Q0 | Q1 | Q2
Initial | x |  |  | 
T1 |  |  |  | 
T2 |  |  |  | 
T3 |  |  |  | 
T4 |  |  |  | 
T5 |  |  |  | 
T6 |  |  |  | 
FF0
FF1
Q0
Q1
D0
D1
FF2
Q2
D0
Data output
CLK
Din
Data Input (Din)
CLK
Data Out (Q2)
Q0
Q1
T1
T2
T3
T4
T5
T6
0
0
0
1
0
1
0
0
0
1
1
0
0
1
0
0
0
0
1
0
1
0
1
1
0
1
0
0
1
0
0
0
1
0
0
0
Slides 13
SERIAL
SERIAL
Notes: 13

## Slide 14: Parallel In Parallel Out Shift Register
All the data bits are entered and available on the output lines simultaneously.
4-bit PIPO shift register using D flip-flops
CLK
D0 Q0
FF0
D2 Q2
FF2
D1 Q1
FF1
D3 Q3
FF3
Qo Q1 Q2 Q3
D0
D1
D2
D3
Q0
Q3
Q2
Q1
CLK
CLK
CLK
CLK
Application: For synchronization of signals and data transfer
Slides 14
Notes: 14

## Slide 15: For the 4-bit PIPO register below, the initial states are given Q0Q1Q2Q3= 1000. what are the outputs of registers immediately after 3rd clock pulse?
Outputs of registers will always be 0011 after first and subsequent clock pulses. Why?
0 0 1 1
1 0 0 0
0 0 1 1
Input data at D is fixed
Input data
Slides 15
Example 4
Notes: 15

## Slide 16: Parallel In Serial Out Shift Register
Loading: Data bits are loaded simultaneously in parallel to their respective flip-flops. This happens when SH/ = 0 and inputs are taken from parallel data QA-QH.
Shifting: Once data is completely stored in the register, it is shifted out serially bit by bit. This happens when SH/ = 1 and input bit for 1st FF is taken from SER input.
Slides 16
Notes: 16

## Slide 17: Parallel In - Serial Out Shift Registers
The circuit uses D flip-flops and NAND gates for entering data (ie writing) to the register.
D0, D1, D2 and D3 are the parallel inputs, where D0 is the most significant bit and D3 is the least significant bit.
To write data in, the mode control line is taken to LOW and the data is clocked in.
The data can be shifted when the mode control line is HIGH as SHIFT is active high.

## Slide 19
S-2 | SLO-1 | Universal Shift Register
 | SLO-2 | Applications of Shift Registers

## Slide 20: Universal Shift Register
The universal shift register can be defined as “The register which can be used to shift the data in both the directions like left, right and can load parallel data as well”.
This register can perform three types of operations, stated below.
  Parallel loading
  Shifting left
  Shifting right.

## Slide 22: Application of Shift Register
Delay line
Serial to parallel converter
Parallel to serial converter
Shift register counter
Sequence generator